## Slide 1: SONATA: Scalable Streaming Analytics for Network Monitoring
Arpit Gupta
Princeton University
Ankita Pawar, Rob Harrison, Rüdiger Birkner,
Marco Canini, Nick Feamster, Jennifer Rexford, Walter Willinger
Notes: ]

## Slide 2
Conventional Network Monitoring
Monitoring
Sensor
Compute
Store
Monitoring
Queries
NetFlow,
sFlow, SNMP, etc.

## Slide 3: Problems with Status Quo
Flexibility:
  Low-level (3rd party/platform-specific) APIs for monitoring queries
  Brittle setup---hard to maintain existing queries or add new ones

## Slide 4: Problems with Status Quo
Flexibility:
  Low-level (3rd party/platform-specific) APIs for monitoring queries
  Brittle setup---hard to maintain existing queries or add new ones
Scalability:
  As Traffic Volume or # Monitoring Queries increases
    Hard to answer queries in real-time
    Hard to transport data from monitoring sensor
Not suited for large networks running
real-time monitoring queries

## Slide 5
Stream Processors to the Rescue!
Monitoring
Sensor
Stream Processor
Runtime
Monitoring
Queries
Packet Tuples

## Slide 6: Changing Status Quo
Flexibility:
  Express Map/Reduce queries for packet tuples
  Not tied to low-level (3rd party/platform-specific) APIs
  Adding new queries is straightforward
Empower Network Operators!

## Slide 7: Is it Scalable?
Use Case:
  Reflection Attack Monitoring Query
    Detect hosts for which # of unique source IPs sending UDP response messages exceeds threshold
  Use two hour IPFIX data trace from a large IXP
Cost:
  Packet Processing: requires processing 220 M tuples per second
Provides flexibility, but scalability is still a challenge for just one query

## Slide 8: Idea 1: Query Partitioning
Observation:
  Data Plane can process packets at line rate
How it works? Map/reduce operations in data plane,
  filter, sample operations for OF-based data plane
  map, reduce, filter, join, sample operations for P4-based data plane
Trade-off:
  Trades packet processing cost with additional state in the data plane

## Slide 9
Query Partitioning in Action
Programmable Data Plane
Data Plane
Configurations
Stream Processor
Runtime
Monitoring
Queries
Runtime Partitions Monitoring Queries
Packet Tuples

## Slide 10: Is it Scalable?
Use Case:
  Reflection Attack Monitoring Query
    Detect hosts for which # of unique source IPs sending UDP response messages exceeds threshold
  Use two hour IPFIX data trace from a large IXP
Costs:
  Packet Processing: 220 M  ~10 tuples per second
  Data Plane State: requires maintaining ~1 B entries in the data plane
How can we strike a balance between the two costs?

## Slide 11: Idea 2: Iterative Refinement
Observation:
  Small fraction of traffic satisfies monitoring queries
How it works:
  Augment operators’ query to observe at coarser level
  Iteratively (over successive window intervals) zoom-in to filter out uninteresting traffic
Trade-off:
  Reduces packet processing & data plane state cost
  Introduces additional detection delay cost

## Slide 12
Iterative Refinement in Action
Programmable Data Plane
Data Plane
Configurations
Stream Processor
Runtime
Monitoring
Queries
Packet Tuples
Stream Processor’s output used by
Runtime to refine queries
Iterative Refinement

## Slide 13: Is it Scalable?
Use Case:
  Reflection Attack Monitoring Query
    Detect hosts for which # of unique source IPs sending UDP response messages exceeds threshold
  Use two hour IPFIX data trace from a large IXP
Costs:
  Packet Processing: ~220 M  ~5 K tuples per second
  Data Plane State: ~1 B  ~12 K entries
  Detection Delay: 2 additional window intervals
Trades pkt processing & data plane state costs for additional detection delay

## Slide 14: SONATA
Scalable Streaming Analytics Platform for Network Monitoring
Application Interface
  Express queries w/o worrying about where and how it will be executed
Runtime
  Iteratively refines and partitions each input query
Data Plane & Streaming Managers
  Compile SONATA queries to target-specific configurations/queries

## Slide 15: SONATA Architecture
Streaming Manager
Programmable Data Plane
Packets
Stream Processor
Application Interface
Queries
Q1
Output Tuples
Input Tuples
Q2
QN
Queries
Runtime
Refinement
Partition
Data Plane Manager
SONATA Queries
Config
Queries

## Slide 16: Changing Status Quo
Flexibility:
  Express Map/Reduce queries over packet tuples
  Don’t worry how or where the query is executed
  Adding new queries and platforms is trivial
Scalability:
  Answers hundreds of queries in real-time for traffic volume as high as few Tb/s
  Strikes a balance between available resources, i.e.
    packets processed by the stream processor
    state required in the data plane

## Slide 17: Summary
SONATA makes it easier to express and scale network monitoring queries using
  Programmable Data Plane
  Scalable Stream Processor
Running Code
  Github: github.com/Sonata-Princeton/SONATA-DEV
  Run test queries or express new ones
Your Network Monitoring Queries?