## Slide 1: Sonata Query-driven Streaming Network Telemetry
Arpit Gupta
Columbia University
UC Santa Barbara
Notes: Today I will present a query-driven network telemetry system that is both flexible as well as scalable

## Slide 2: Network Management
Google
Cogent
Level3
Princeton
Outages
Congestion
Cyberattacks
Network Operator
Detect network events in real time
Notes: The onus of making the net work is on network operators managing these networks.
However, in recent years with the exponential growth in Internet-connected devices and applications, the complexity of network management has increased significantly.
To keep the network running, they need continuously handle various network events such as outages, network congestion, and cyber attacks.
To handle all these events, they need to detect these events in real time, ie perform network monitoring.

## Slide 3: Network Monitoring Requirements
👺
😵
Src: Victim
Dst: DNS
Src: Victim
Dst: DNS
Src: DNS
Dst: Victim
Src: DNS
Dst: Victim
DNS
DNS
Attacker
Victim
Receive
DNS responses from many distinct sources
jitter
distinct hosts
volume
delay
loss
…
Metrics
address
protocol
payload
device
location
…
Traffic
Flexible network monitoring is desired
Notes: To better understand the requirements of a network monitoring system,
Let us consider a network task where the operators wants to know whether any host in the network is a victim of a DNS Reflection attack.
2. In this attack, an attacker sends spoofed DNS requests to public DNS resolvers,
3. Response to these requests get reflected to the victim, who becomes overwhelmed as the number of responses grow large
4.To detect victims of such an attack, network operator needs to identify hosts that receive DNS responses from too many unique sources
5. Note that here, network operator is trying to extract an aggregate metric from a subset of traffic.
6. In general, there are so many ways in which network operators would like to specify which subset of traffic it is interested in, and which metric it wants to extract.
7. Thus, it is critical that network monitoring systems are as flexible as possible.

## Slide 4: Network Monitoring with Sonata
Malware Detection
Performance Diag..
DDoS Detection
Fault Localization
Flexibility
Scalability
Abstractions
Algorithms
System
Sonata
Notes: 1.To efficiently monitor wide range of network events, on one hand monitoring systems need to support limitless creativity, letting operators express queries to figure out what’s going on in the network
2. But, on the other hand network monitoring systems only have limited compute and storage resources to use.
3. This creates a fundamental gap between desired flexibility and scalability.
4. In today’s talk, I will show how Sonata fills this gap.
5. More specifically, I will show how we designed programming abstractions that made it easier for network operators to express queries for network monitoring.
6. Algorithms that we developed to make the best use of limited compute and storage resources;
7. And the system we built that glues the high-level abstractions to the low-level algorithms.

## Slide 5: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high-volume traffic in real time?
Notes: Clearly building such a flexible and scalable network-monitoring system is challenging.
It requires addressing two key challenges: how to let network operators express queries for a wide-range of monitoring tasks with as much flexibility as possible?
And then figure out how to scale the execution of these flexible queries for high volume traffic and that too in real-time.

## Slide 6: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high-volume traffic in real time?
Notes: So let’s first talk about the programming abstractions.

## Slide 7: Packet as Tuple
Header
Metadata
Payload
Packet
traversed path, queue size, number of bytes, …
source/ destination address, protocol, ports, …
Packet = (path, qsize, nbytes,…
sIP, dIP, proto, sPort, dPort, …
payload)
Treat packet as a tuple
Notes:   1 Packets in the network not only carry information in their header fields and payload, but also the meta information about the state of the underlying network, such as the time when a packet arrives at a switch or number of hops it traversed in the network etc.
  2. Unlike many existing network monitoring systems, that operate at coarser level of granularity, Sonata lets network operators treat packet fields as tuple, capturing all the required information.

## Slide 8: Monitoring Tasks as Dataflow Queries
Detecting DNS Reflection Attack
Identify if DNS response messages from unique DNS servers to a single host exceeds a threshold (Th)
pVictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
DNS Responses
from Unique DNS Servers
to a Single Host
exceeds a Threshold
Notes:   It then lets them apply familiar dataflow operators such as map, reduce, filter, join etc. over the stream of packet tuples to express a wide-range of monitoring queries.
  Let me illustrate the point with a familiar example
  … improvise
  Emphasize that this abstractions ensures that we can express a wide-range of monitoring tasks now.

## Slide 9: Monitoring Tasks as Dataflow Queries
Confirm DNS Reflection + Amplification Attack
Identify if the number of response type of RRSIG for victims of DNS reflection attack exceeds threshold Th2
victimIPs = pktStream
.filter(p => p.udp.sport == 53)
.join(pVictimIPs, key=‘dstIP’)
.filter(p => p.dns.rr.type == RRSIG)
.map(p => (p.dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th2)
Express wide range of network monitoring tasks in fewer than 20 lines of code
Notes:   It then lets them apply familiar dataflow operators such as map, reduce, filter, join etc. over the stream of packet tuples to express a wide-range of monitoring queries.
  Let me illustrate the point with a familiar example
  … improvise
  Emphasize that this abstractions ensures that we can express a wide-range of monitoring tasks now.
    .filter(p => p.dns.rr.type == RRSIG)
    .map(p => (p.dstIP, 1))
    .reduce(keys=(dstIP,), sum)
    .filter((dstIP, count) => count > T2)
    .map((dstIP, count) => dstIP)

## Slide 10: Building Sonata is Challenging
Programming abstractions
  How to let network operators express queries for a wide-range of monitoring tasks?
Scalability
  How to execute multiple queries for high-volume traffic in real time?
Notes: Allowing operators to express their program processing all the packets in the network sets us up for a huge scalability challenge.
Now we need to figure out how we can execute these flexible queries for high-volume traffic and that too in real time.

## Slide 11: Where to Execute Monitoring Queries?
  Univmon [SIGCOMM’16]
  Marple [SIGCOMM’17]
  Gigascope [SIGMOD’03]
  NetQRE [SIGCOMM’17]
Match | Headers + Payload
Actions | Any
State | O(Gb)
Speed | O(μs)
Headers++
add, subtract, bit operations
O(Mb)
O(ns)
Switches
CPUs
Can we use both switches and CPUs?
Notes: The first question we need to answer here is which target should we use to execute these flexible queries?
One option is to use CPU, they can match on both header as well as payload fields, they can perform any operation over the packet, and can support stateful operations that require Gbs of memory.
But, their packet -processing capability is very slow.
One can leverage advances made in the area of scalable stream processing to horizontally scale the computations,
But, as they are not in-network solutions, they incur significant bandwidth costs
The other option is programmable switches, though they can process packets at line rate, but they offer limited packet-processing and storage capabilities.
Thus, unlike existing network-monitoring systems, we explored the idea of using both the targets for query execution, extracting the best of both worlds.

## Slide 12: PISA* Processing Model
Programmable Deparser
Stages
ip.src=1.1.1.1
ip.dst=2.2.2.2
...
Packet Header Vector
Programmable Parser
Memory
Persistent State
ALU
  *RMT [SIGCOMM’13]
Notes: Modern Protocol Independent Switch Architecture devices consist of a programmable parser,
that can process user-defined packet formats and stores the parsed header fields in a fixed-length packet header vector
A switch has multiple processing stages, each consisting of multiple reconfigurable match-action tables implemented using a block of TCAM memory, Arithmetic-Logic-Units for processing, and a limited amount of persistent state as SRAM memory.
A pipeline consists of a fixed number of these stages, followed by
A programmable deparser, that serializes a new packet out of the transformed packet header vector.
Given this background, let’s compare the packet-processing model of PISA switches with the dataflow processing model inherent to stream processors.

## Slide 13: Mapping Dataflow to Data plane
Which dataflow operators can be compiled to match-action tables?
 | Dataflow | Data plane
Model | Pipeline | Pipeline
Processing Unit | Operators | Match-Action Tables
Structured Data | Tuples | Packets
Notes: Both dataflow and data plane processing models can be represented as a pipeline of processing units that transform some structured data.
In the dataflow model, these processing units are dataflow operators such as filter, map, and reduce. In the data plane, they are match-action tables.
Dataflow processing pipelines apply transformations over stream of tuples, and switches apply transformations over packets.
Though representing packet as a tuple is straightforward, but figuring out how to compile dataflow operators to match-action tables is non-trivial.

## Slide 14: Compiling Individual Operators
filter(p)
Stream of elements
Elements satisfying
predicate (p)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
1
2
3
4
5
6
7
Match | Action
p | 
udp.sport == 53 | 
Notes: Let's start by looking at what it takes to compile individual operators to match-action tables, one at a time.
The filter operator takes
a stream of elements as input, and returns
the set of elements that satisfy some predicate p.
We can implement this with match-action tables by simply supplying p as the match component.
If we return to the DNS reflection query we saw earlier, the predicate performs an exact match on the UDP source port.
We would implement this [🌀] directly in the match-action table as shown.

## Slide 15: Compiling Individual Operators
reduce(f)
Match | Action
* | idx = hash(m.dstIP)
Input
Output
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Stream of elements
Result of applying
function f over all elements
Memory
Match | Action
* | stateful[idx] += 1
1
2
3
4
5
6
7
Notes: The reduce operator also takes a stream of elements as input and returns a single result that is the application of the function f over all elements.
Naturally, we break up the stream into windows of size (W) seconds to compute this function over a finite stream.
Unlike map and filter, the reduce function requires some memory to store the intermediate value of the function between the arrival of successive elements.
Like the map operator, we would also apply the function f in the action body of a match-action table, but since stateful memory is implemented as a hash-table in PISA switches, we must first compute an index into the hash table before looking up the value stored in it.
In the case of our example query,
  the first table computes an index by hashing the key of interest, in this case dstIP.
  The second table applies the function (sum) to the intermediate value and the next element (1).

## Slide 16: Compiling a Query
Programmable Deparser
Stages
Programmable Parser
State
Filter Map
Filter
D1
D2
Map
R1
R2
Notes: To compile an entire query, we would just sequentially apply [🌀] the set of match-action tables generated by each individual operator. Here the D1/D2 and R1/R2 abbreviate the first and second tables of the distinct and reduce operators, respectively.

## Slide 17: Query Partitioning Decisions
Query Planner
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Resources?
Reduce Load?
Tuples
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
pvictimIPs = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map((dstIP, srcIP) => (dstIP, 1))
.reduce(keys=(dstIP,), sum)
.filter((dstIP, count) => count > Th)
Notes: So far, we’ve seen how we can compile a query to a sequence of match action tables in the switch
However, as the switches have limited compute and storage resources, system’s query planner decides how to partition the query between the switch and the stream processor
After executing the subset of dataflow operators, the switch sends the output tuples to the stream processor for further processing..
There are many ways in which the query planner can partition the given query, for each partitioning decision, it needs to answer two questions:
  Whether the switch has enough resources to execute the partitioned queries, and
  Whether the partitioning decision minimizes the load on the stream processor?
The decision making might look simpler for a single query, but note that query planner needs to make partitioning decision for multiple queries.

## Slide 18: Query Partitioning ILP
Constraints
Goal: Minimize tuples sent to stream processor
Programmable Deparser
Stages
Programmable Parser
Memory
Persistent State
ALU
PHV Size
Number of
Actions
Total Stages
Stateful Memory
Packet Header Vector
Notes: We model this query-partitioning problem as an Integer-Linear-Program.
Here, query planner’s goal is to minimize the number of tuples sent to the stream processor subject to the [🌀] constraints of the underlying data plane target.
More concretely, we take into consideration: the size of the packet header vector, the number of actions per stage, the amount of stateful memory per stage, and the total number of stages
The query planner uses representative packet traces to estimate the resource requirements for individual operators and how partitioning decisions affect the load at the stream processor.

## Slide 19: How Effective is Query Partitioning?
Chart: # Tuples at Stream Processor
| CPU-Only
Number of Packet Tuples | 1000000000 | 1
Log Scale
8 Tasks, 100 Gbps Workload
O(1 B)
Notes: Explain the graph and setup
Build intuition that we expect multiple orders of magnitude reduction

## Slide 20: How Effective is Query Partitioning?
Chart: # Tuples at Stream Processor
| CPU-Only | Paritioning
Number of Packet Tuples | 1000000000 | 100000000
Log Scale
O(1 B)
O(100 M)
Only one order of magnitude reduction
8 Tasks, 100 Gbps Workload
Notes: Argue that one order is not enough.
Let’s try to understand why we don’t see expected gains with query partitioning.

## Slide 21: Query Partitioning Limitations
Filter Map
Filter
D1
D2
Map
R1
R2
distinct
reduce
How can we reduce the
memory footprint of stateful operators?
Notes: We observed that for many stateful operations, the amount of stateful memory required was more than what’s available in the switch.
We then started exploring how we can reduce the memory footprint of stateful operators.

## Slide 22: Observations: Nature of Monitoring Tasks
DNS Reflection Attack Victims
All Hosts
Most monitoring tasks are looking for needles in a haystack
Notes:   We observed that most monitoring tasks are looking for a needle in a haystack. For example, for the reflection attack query, there are only few victims compared to millions of hosts in the network. The question is, how can we avoid wasting limited resources over haystack and focus on those tiny needles.

## Slide 23: Observations: Possible to Reduce Memory Footprint
Detecting DNS Reflection Attack
victim = pktStream
.map(dIP => dIP/8)
      .filter(p => p.udp.sPort == 53)
      .map(p => (p.dIP, p.sIP))
      .distinct()
      …
Only consider first 8 bits
Queries at coarser levels have smaller memory footprint
Notes: We also observed that executing queries at coarser levels have smaller memory footprint

## Slide 24: Observations: Possible to Preserve Query Accuracy
Detecting DNS Reflection Attack
victim = pktStream
.map(dIP => dIP/8)
      .filter(p => p.udp.sPort == 53)
      .map(p => (p.dIP, p.sIP))
      .distinct()
      …
Hierarchical packet field
Query accuracy is preserved if refined with hierarchical packet fields
Notes: Packet field dstIP is hierarchical in nature. This ensures that executing queries at coarser levels does not miss the needles of interest.
There are more packet fields that have hierarchical structure such as source IP address, domain name state, location etc.
Now let’s see how we can use these observation to scale query execution.

## Slide 25: Iterative Query Refinement
Filter
D1
D2
Map
R1
R2
Packet Stream
t+W
Map
Filter Map
Window
map(dIP=>dIP/8)
PISA Target
First, execute query at coarser level

## Slide 26: Iterative Query Refinement
Filter
D1
D2
Map
R1
R2
Filtered
Packet Stream
Map
Filter Map
Detection
Delay
Filter
Filter Map
Filter
D1
D2
Map
R1
R2
t+2W
Smaller
memory footprint
PISA Target
Then, execute query at finer level(s)
Smaller memory footprint at
the cost of additional detection delay

## Slide 27: Query Planning Problem
Goal
  Minimize tuples sent to the stream processor
Given
  Queries, packet traces
Determine
  Which packet field to use for iterative refinement?
  What levels to use for iterative refinement?
  What’s the partitioning plan for each refined query?
Augment partitioning ILP to compute both refinement and partitioning plans
Notes: Automatically deciding which query to refine iteratively, which packet field to use for refinement, and how to make query-specific refinement plans w/o requiring any input from network operators is non-trivial.
Now that we understand how Sonata makes partitioning and refinement plans, let’s see how efficient are these two techniques to reduce the workload at the stream processor.

## Slide 28: Sonata’s Performance
Chart: # Tuples at Stream Processor
| CPU-Only | Paritioning | Partitioning + Refinement
Number of Packet Tuples | 1000000000 | 100000000 | 100000
Log Scale
8 Tasks, 100 Gbps Workload
O(1 B)
O(100 M)
O(100 K)
Up to 4 orders of magnitude reduction

## Slide 29: Sonata’s Architecture
Streaming Driver
Programmable Data Plane
Packets In
Stream Processor
Query Interface
Queries
Q1
Output
Tuples
Q2
QN
Queries
Core
Data Plane Driver
Packets Out
Query Partitioning
Iterative Refinement
Notes: Single switch setup

## Slide 30: Future Directions

## Slide 31: Extend Packet Parser
Currently, dns.rr.type is parsed in user-space
Possible to parse it in the data plane itself
Layers of Interest:
  DNS
  SMTP
  …
victimIPs(t) = pktStream(W)
    …
    .filter(p => p.dns.rr.type == RRSIG)
    …

## Slide 32: Extend Dataflow Operators
Existing Operators
  Reduce
    Currently, only sum function is supported
    Implement more complex aggregation functions
  Join
    Currently, only executed in user space
    Compiler subset of join operators in switch
New Operators
  Flat Map
  Sample

## Slide 33: Example: Isolate Video Streaming Traffic
Detect hosts that receive DNS response messages from known video streaming services
vidFlows = pktStream
    .filter(p => p.udp.sport == 53)
    .map(p => (p.dns.qname, p.5-tuple))
    .join(known_vid_services, key=‘qname’)
    .map(p => (p.5-tuple))

## Slide 34: Support Network-Wide Queries
Extend Query Interface
  Query all packets at any location
  Extract path-related fields, e.g. queue lengths, …
Scale Query Execution
  Synthesize queries to minimize coordination overhead
  Determine where to execute each operator
  Use spatial hierarchy for iterative refinement
  Dynamically route packets for processing
Notes: , e.g. traversed hops, queue lengths per hop, path latency etc.

## Slide 35: Example: Localize Bottlenecked Switches
Detect switches responsible for performance degradation of video streaming flows
Switches= pktStream
    .filter(p => p.tcp.sport == 80)
    .map(p => ((p.5-tuple,p.path),p.nBytes))
    .join(vidFlows, key=((5-tuple,))
    .reduce(key=((5-tuple,), sum)
    .filter(p => p.dataRate> T1)
    .flatmap(p =>(p.swid, 1))
    .reduce(key=((swid,), sum)
    .filter(p => p.count > T2)

## Slide 36: Enable Intelligent Network Monitoring
Learning and Query Planning Disconnect
  Most learning models are cost-agnostic
  Query planning assumes learning models are know
  Results in accurate but prohibitively costly models
Opening the Learning Blackbox
  Let operators specify related queries (features)
  Synthesize coarser-granularity queries (low cost)
  Design cascade of classifiers (cheap  expensive)
Notes: , e.g. traversed hops, queue lengths per hop, path latency etc.

## Slide 37: Example: Intelligent Network Monitoring
DNS Reflection + Amplification Attack
feature1 = pktStream
.filter(p => p.udp.sport == 53)
.map(p => (p.dstIP, p.srcIP))
.distinct()
.map(p => (p.dstIP, 1))
.reduce(keys=(dstIP,), sum)
feature2 = pktStream
.filter(p => p.udp.sport == 53)
.filter(p => p.dns.rr.type == RRSIG)
.map(p => (p.dstIP, 1))
.reduce(keys=(dstIP,), sum)
Notes:   It then lets them apply familiar dataflow operators such as map, reduce, filter, join etc. over the stream of packet tuples to express a wide-range of monitoring queries.
  Let me illustrate the point with a familiar example
  … improvise
  Emphasize that this abstractions ensures that we can express a wide-range of monitoring tasks now.
    .filter(p => p.dns.rr.type == RRSIG)
    .map(p => (p.dstIP, 1))
    .reduce(keys=(dstIP,), sum)
    .filter((dstIP, count) => count > T2)
    .map((dstIP, count) => dstIP)

## Slide 38: Summary
Sonata is:
  Flexible
    Dataflow queries over packet tuples
    Fewer than 20 lines of code
  Scalable
    Query refinement & partitioning algorithms
    4 orders of magnitude workload reduction
Future Directions
  Extend packet parser and dataflow operators
  Support network-wide queries
  Enable intelligent network monitoring
https://sonata.cs.princeton.edu
https://github.com/sonata-princeton
Notes: We have designed and implemented a query-driven network monitoring system which is
  Flexible, network operators can express wide range of monitoring tasks as dataflow queries over packet tuples in less than 20 lines of code
  Scalable, which uses query partitioning and refinement algorithms to reduce the workload by 4 orders of magnitude.
Though Sonata is a step forward in the right direction, it provides a foundation for much future work.